Q1.          (a)     The drawing shows a small transformer used to recharge the battery in a 4.2 V mobile phone from a 230 V mains supply.

Explain how you know that this is a step-down transformer.

.....................................................................................................................................

.....................................................................................................................................

(1)

(b)     A transformer consists of an insulated coil of wire, called the primary coil, on one side of a core. Another coil of insulated wire, called the secondary coil, is on the other side.

Give two features of the core.

1 ..................................................................................................................................

2 ..................................................................................................................................

(2)

(Total 3 marks)

Q2.          The drawing shows an experiment using a low voltage supply, a joulemeter, a small immersion heater and a container filled with water.

The immersion heater is designed for use in a tropical fish tank. It is connected to a step-down transformer supplied by 230 V a.c. mains.

The inside of a step-down transformer consists of three main parts. Name the three parts and briefly describe them. You may add to the diagram to help you to answer.

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

(Total 4 marks)

Q3.          Circuit breakers help to make the electricity supply in homes safer.
A circuit breaker is an automatic safety switch. It cuts off the current if it gets too big.

Describe, in as much detail as you can, how this circuit breaker works.

To gain full marks in this question you should write your ideas in good English. Put them into 
a sensible order and use the correct scientific words.

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

(Total 6 marks)

Q4.          A fault in an electrical circuit can cause too great a current to flow.
Some circuits are switched off by a circuit breaker.

One type of circuit breaker is shown above. A normal current is flowing.
Explain, in full detail, what happens when a current which is bigger than normal flows.

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

(Total 4 marks)

Q5.          The diagram below shows a door lock which can be opened from a flat inside a building.

(a)     Explain how the door is unlocked when the switch is closed.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(4)

(b)     State two changes which would increase the strength of the electromagnet.

1 ..................................................................................................................................

2 ..................................................................................................................................

(2)

(c)     Why is the spring needed in the lock?

....................................................................................................................................

....................................................................................................................................

(1)

(d)     The connections to the coil were accidentally reversed. Would the lock still work?

....................................................................................................................................

Explain your answer.

....................................................................................................................................

....................................................................................................................................

(2)

(Total 9 marks)

Q6.          The diagram shows apparatus used to demonstrate the motor effect. X is a short length of bare copper wire resting on two other wires.

(a)     (i)      Describe what happens to wire X when the current is switched on.

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

(ii)     What difference do you notice if the following changes are made?

A       The magnetic field is reversed.

...........................................................................................................................

...........................................................................................................................

B       The current is increased.

...........................................................................................................................

...........................................................................................................................

(3)

(b)     The diagram shows a coil placed between the poles of a magnet. The arrows on the sides of the coil itself show the direction of the conventional current.

The arrows labelled F show the direction of the forces acting on the sides of the coil. Describe the motion of the coil until it comes to rest.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(c)     Most electric motors use electromagnets instead of permanent magnets. State three of the features of an electromagnet which control the strength of the magnetic field obtained.

1 ................................................................................................................................

2 ................................................................................................................................

3 ................................................................................................................................

(3)

(Total 9 marks)

Q7.          (a)     An appliance in a house has a transformer. The transformer is used to reduce the voltage to the level needed by the appliance.

The diagram shows the transformer.

(i)      Name the material used for the core of the transformer.

...........................................................................................................................

(1)

(ii)     The transformer has 10 000 turns on the input side and 2000 turns on the output side. If the mains voltage of 240 volts is applied to the input, calculate the output voltage. You may find the following information helpful:

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

(3)

(b)     Explain, in terms of magnetic fields, how a transformer works.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(4)

(c)     A 12 V car battery is connected to the input leads of the transformer. It is hoped to reduce the voltage to 2.4 V in order to run a small motor. When the output voltage is measured it is found to be zero.

Explain why the output voltage is zero.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 10 marks)

Q8.          The diagram below shows a transformer.

(i)      Name the material used to make the core of the transformer.

.....................................................................................................................................

(1)

(ii)      The primary coil has 48 000 turns and the secondary coil 4000 turns.

If the input voltage is 240 V a.c., calculate the output voltage.

.....................................................................................................................................

.....................................................................................................................................

Answer ......................................... V

(2)

(iii)     Explain how the use of such a transformer could be adapted to transform a low voltage into a higher voltage.

.....................................................................................................................................

.....................................................................................................................................

(1)

(Total 4 marks)

Q9.          The diagram shows a switch that is operated by an electromagnet.

(i)      What is this type of switch called?

.....................................................................................................................................

(1)

(ii)      The switch is used in a car starter motor circuit.

Explain how turning the ignition key makes a current flow in the starter motor. The explanation has been started for you.

When the ignition key is turned ..................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(Total 4 marks)

Q10.          The diagram shows apparatus used to demonstrate the electric motor effect. When he switch is closed the wire moves.

(i)      Draw an arrow on the diagram to show the direction the wire moves.

(1)

(ii)      Explain why the wire moves.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 3 marks)

Q11.          (a)     The diagram represents a simple transformer used to light a 12 V lamp. When the power supply is switched on the lamp is very dim.

(i)      Give one way to increase the voltage at the lamp without changing the power supply.

............................................................................................................................

............................................................................................................................

(1)

(ii)     What is meant by the iron core being laminated?

............................................................................................................................

............................................................................................................................

(1)

(b)     Electrical energy is distributed around the country by a network of high voltage cables.

(i)      For the system to work the power is generated and distributed using alternating current rather than direct current. Why?

............................................................................................................................

............................................................................................................................

(1)

(ii)     Transformers are an essential part of the distribution system. Explain why.

............................................................................................................................

............................................................................................................................

............................................................................................................................

(2)

(iii)     The transmission cables are suspended high above the ground. Why?

............................................................................................................................

(1)

(c)     The power station generates 100 MW of power at a voltage of 25 kV. Transformer A, which links the power station to the transmission cables, has 44 000 turns in its 275 kV secondary coil.

(i)      Write down the equation which links the number of turns in each transformer coil to the voltage across each transformer coil.

............................................................................................................................

............................................................................................................................

(1)

(ii)     Calculate the number of turns in the primary coil of transformer A. Show clearly how you work out your answer.

............................................................................................................................

............................................................................................................................

............................................................................................................................

Number of turns = ........................................

(2)

(d)     The diagram shows how the cost of transmitting the electricity along the cables depends upon the thickness of the cable.

(i)      Why does the cost due to the heating losses go down as the cable is made thicker?

............................................................................................................................

(1)

(ii)     By what process is most heat energy lost from the cables?

............................................................................................................................

(1)

(Total 11 marks)

Q12.          A transformer is used to reduce the 230 V a.c. mains to the 12 V supply required for the lighting system. The transformer has 1150 turns on its primary coil.

(i)      Write down the equation which links the number of turns of each transformer coil to the voltage across each transformer coil.

....................................................................................................................................

....................................................................................................................................

(1)

(ii)      Calculate the number of turns on the secondary coil of the transformer. Show clearly how you work out your answer.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

number of turns on the secondary coil = .........................

(2)

(Total 3 marks)

Q13.          (a)     Name a material that could be used to make the outside case of the plug.

.....................................................................................................................................

Give a reason for your choice.

.....................................................................................................................................

.....................................................................................................................................

(2)

(b)     To gain full marks in this question you should write your ideas in good English. Put them into a sensible order and use the correct scientific words.

Some electrical circuits are protected by a circuit breaker. These switch the circuit off if a fault causes a larger than normal current to flow. The diagram shows one type of circuit breaker. A normal current (15 A) is flowing.

Source: adapted from V. PRUDEN and K. HIRST, AQA GCSE Sceince
Reproduced by permission of Hodder and Soughton Educational Ltd

Explain what happens when a current larger than 15A flows. The answer has been started for you.

When the current goes above 15 A, the electromagnet becomes stronger and

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(Total 5 marks)

Q14.          (a)     This notice is on the back of a television set.

The transformer used in the television set has 75 turns on its primary coil. The potential difference (p.d.) across the primary coil is 230 volts and the p.d. across the secondary coil is 32 200 volts.

Use the equation below to calculate the number of turns on the secondary coil.

Show clearly how you work out your answer.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

Number of turns on the secondary coil = ....................

(2)

(b)     The diagram shows the structure of a transformer.

Explain how the transformer works.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(3)

(Total 5 marks)

Q15.          The diagram shows the design for a remotely controlled door bolt.

When the correct numbers are entered into the keypad the transformer switches on. Then the door can be opened.

(a)     What kind of transformer is shown in the diagram?

....................................................................................................................................

(1)

(b)     What does the abbreviation a.c. stand for?

....................................................................................................................................

(1)

(c)     Complete the sentences using the correct words from the box.

attracts downwards magnet reflects repels sideways switch transformer upwards

(i)      When a current flows in the coil, the coil becomes a ................................... .

(ii)     The coil ................................... the iron bolt which moves ............................

(3)

(Total 5 marks)

Q16.          (a)     The diagram shows a transformer.

(i)      Is the transformer in the diagram being used as a step-up transformer or as a step-down transformer?

Put a tick () in the box next to your answer.

a step-up transformer

a step-down transformer

Explain your answer.

...........................................................................................................................

...........................................................................................................................

(1)

(ii)     Why is insulated wire, and not uninsulated wire, used to make the coils?

...........................................................................................................................

...........................................................................................................................

(1)

(iii)     Why is the core made of iron?

...........................................................................................................................

...........................................................................................................................

(1)

(b)     A transformer has 500 turns on its primary coil and 7500 turns on its secondary coil. The potential difference across the primary coil is 150 volts.

Use the equation in the box to calculate the potential difference across the secondary coil.

Show clearly how you work out your answer.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

Potential difference across the secondary coil = .............................. volts

(2)

(c)     Step-down transformers are used between power lines and people’s houses.

Explain why.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(d)     Before 1926, large towns had their own local power stations. After 1926, these power stations were connected to form the National Grid.

Explain the advantage of having a National Grid system.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 9 marks)

Q17.          When a conductor carrying an electric current is placed in a magnetic field a force may act on it.

(a)     State two ways in which this force can be increased.

1 ..................................................................................................................................

2 ..................................................................................................................................

(2)

(b)     State two ways in which this force can be made to act in the opposite direction.

1 ..................................................................................................................................

2 ..................................................................................................................................

(2)

(c)     In what circumstance will no force act on a conductor carrying an electric current and in a magnetic field?

.....................................................................................................................................

.....................................................................................................................................

(1)

(Total 5 marks)

Show clearly how you work out your answer.

.....................................................................................................................................

.....................................................................................................................................

Kinetic energy = ............................................... J

(2)

(Total 7 marks)

Q18.          (a)     The diagram shows a transformer.

(i)      What is part A?

...........................................................................................................................

(1)

(ii)     What is part B and what is it made of?

...........................................................................................................................

...........................................................................................................................

(2)

(iii)     When there is an alternating current in the primary coil, what is produced in part B?

...........................................................................................................................

...........................................................................................................................

(2)

(b)     Transformers are used in the National Grid. The diagram shows part of the National Grid.

Complete the two spaces in the sentence.

Transformer C is a ............................................. transformer and transformer D is

a ............................................. transformer.

(1)

(c)     This is an item from a newspaper.

Which two suggestions would reduce the possible risk to people’s health?
Put a tick () in the box next to your answers.

Do not build new houses near to existing power lines.

Move the power lines so that they take the shortest routes.

Move each power station to the centre of the nearest city.

Build new power lines away from where people live.

Use more transformers in the National Grid.

(2)

(Total 8 marks)

Q19.          (a)     The basic structure of a transformer is a primary coil of insulated wire, an iron core and a secondary coil of insulated wire.

(i)      Why is the core made of iron?

...........................................................................................................................

...........................................................................................................................

(1)

(ii)     Explain how a transformer works.

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

(4)

(b)     A small step-down transformer is used in the charger for an electric screwdriver.

The input to the transformer is 230 V a.c. mains supply and the output is 5.75 V a.c.
There are 3200 turns on the primary coil.

Use the equation in the box to calculate the number of turns on the transformer’s secondary coil.

Show clearly how you work out your answer.

.....................................................................................................................................

.....................................................................................................................................

Number of turns = ..............................

(2)

(Total 7 marks)

Q20.          Many electrical appliances use the circular motion produced by their electric motor.

(a)     Put ticks () in the boxes next to all the appliances in the list which have an electric motor.

| electric drill |  |
| --- | --- |
| electric fan |  |
| electric food mixer |  |
| electric iron |  |
| electric kettle |  |
| electric screwdriver |  |

(2)

(b)     One simple design of an electric motor is shown in the diagram. It has a coil which spins between the ends of a magnet.

(i)      Give two ways of reversing the direction of the forces on the coil in the electric motor.

1 ........................................................................................................................

...........................................................................................................................

2 ........................................................................................................................

...........................................................................................................................

(2)

(ii)     Give two ways of increasing the forces on the coil in the electric motor.

1 ........................................................................................................................

...........................................................................................................................

2 ........................................................................................................................

...........................................................................................................................

(2)

(Total 6 marks)

Q21.          The diagram shows the basic structure of a transformer.

(a)     Explain how a transformer works.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

(5)

(b)     A transformer is used to change the 230 volt mains electricity supply to the 12 volts needed to operate a low voltage halogen lamp. The current through the halogen lamp is 
4 amps.

Calculate the current drawn by the transformer from the mains electricity supply.

Assume that the transformer is 100 % efficient.

Write down the equation you use, and then show clearly how you work out your answer.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

Current = ........................................... amps

(2)

(Total 7 marks)

Q22.          In this question you will be assessed on using good English, organising information clearly and using specialist terms where appropriate.

The diagrams show a relay switch and how it is used in a car ignition circuit.

Turning the ignition key closes the ignition switch.
Explain how this causes the starter motor to operate.

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

.................................................................................................................................

(Total 6 marks)

Q23.         The diagram shows the equipment used by a student to investigate the strength of five different electromagnets.

The stronger the electromagnet, the more paper clips it will hold.

(a)     Why is it important that the paper clips used in the investigation are all the same size?

........................................................................................................................

........................................................................................................................

........................................................................................................................

(1)

(b)     The five electromagnets, J, K, L, M and N, used by the student are shown below.
Each electromagnet was made by wrapping lengths of insulated wire around identical iron nails.

The student wants to find out how the strength of an electromagnet depends on the number of turns of wire in the coil.

Which electromagnets should the student compare in order to do this?

........................................................................................................................

(1)

(c)     The student concluded:

“The strength of an electromagnet is always directly proportional to the number of turns on the coil.”

(i)      Explain how the data from the investigation supports the student’s conclusion.

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

(2)

(ii)     The student makes one more electromagnet by winding 100 turns onto a nail.

Before testing the electromagnet, the student predicted the number of paper clips that the electromagnet would hold when the current is 1 amp.

How many paper clips should the student predict that the electromagnet would hold?

Show clearly how you work out your answer.

...............................................................................................................

...............................................................................................................

...............................................................................................................

number of paper clips = .....................................

(2)

(iii)     When the student tested the electromagnet it held 20 paper clips.
This is not what the student predicted.

Explain what the student should do when new data does not seem to support the prediction that was made.

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

...............................................................................................................

(3)

(Total 9 marks)

Q24.         The diagram shows a transformer made by a student. The student has designed the transformer to make a 6 V light bulb work using a 2 V power supply.

(a)     Draw a ring around the correct answer to complete the following sentences.

| (i) For the transformer to work, the student | must use an a.c. can use either an a.c or a d.c. must use a d.c. |
| --- | --- |

power supply.

(1)

(ii)     On the primary coil there are 30 turns of wire. For the lamp to work brightly

|  | less than 30 exactly 30 more than 30 |  |
| --- | --- | --- |
| there must be |  | turns of wire on the secondary coil. |

(1)

(b)     What is the transformer core made from?

Give a reason for your answer.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

(2)

(Total 4 marks)

M1.          (a)     output voltage less than (the) input voltage

or p.d. across output less that p.d.

across input or output is (only) 4.2 V

(whereas) the input is 230V

or WTTE (words to that effect)

1

(b)     any two from

(made of soft) iron

laminated

or designed to reduce eddy currents

or made of thin slices with slices of insulating material between them

core(s) joined to make a ring

2

[3]

M2.

each mark may be gained from a written description or from a caption on the diagram or from both together but do not credit if there is any contradiction between them

one coil on each side

1

of insulated wire

or insulated coil

1

number of turns on primary coil/coil 1/input coil greater than number of
turns on the secondary coil/coil 2/output coil

this must be clear for example do not credit more coils do not credit bigger coil

1

core of laminated iron

or core of (soft) iron

1

[4]

M3.          Quality of written communication: One mark for correct sequencing.
bolt out ® plunger up ® switch off / circuit broken

1

any five from

•        high current flows

•        electromagnet is stronger

•        the iron bolt is pulled out

•        the plastic plunger moves up

•        the switch is lifted / open / off

accept circuit is broken

•        no current flowing

•        to re-set the plunger must be pushed down

5

[6]

M4.          electromagnet becomes stronger  (not becomes magnetic) iron moves left – implied OK
plunger goes up push switch goes to off or circuit broken unless plunger moves down

for 1 mark each

[4]

M5.          (a)     current flows
coil / core magnetised / electromagnet activated / energised / turned on
attracts iron bar causing bolt to be pulled out

each for 1 mark

4

(b)     more turns
bigger current / e.m.f
softer iron core

any two for 1 mark each

2

(c)     to relock door / return iron bar / to lock door

for 1 mark

1

(d)     iron bar would still be attracted / coil still magnetised so still works

for 1 mark each

yes + wrong answer

0 marks

yes + current still flows

1 mark

yes + still magnetised / iron bar still attracted

2 marks

2

[9]

M6.          (a)     (i)      it moves or experiences a force horizontally to the right

for 1 mark

1

(ii)     A – moves in opposite direction or force reversed e.c.f. 
B – faster movement or larger force
(not move further)

for 1 mark each

2

(b)     turns clockwise
oscillates/reverses
comes to rest facing field/at 90o to field/vertically

for 1 mark each

3

(c)     number of turns or linear number density of turns current core

for 1 mark each

3

[9]

M7.          (a)     (i)      Iron

for 1 mark

1

(ii)     V/240 = 2000/10 000
V = 48
V

for 1 mark each

3

(b)     changing current in primary causes changing (magnetic) field in core links to secondary inducing voltage (emf) in secondary (NOT current) secondary voltage/current is alternating

for 1 mark each

4

(c)     magnetic field not changing/no electromagnetic induction because direct current

for 1 mark each

2

[10]

M8.          (i)      iron

for 1 mark

1

(ii)      20

gains 2 marks

else working

gains 1 mark

2

(iii)     reverse input/output

for 1 mark

or increase secondary turns

1

[4]

M9.          (i)      relay

accept solenoid

do not accept magnetic switch

1

(ii)      a current flows through the coil (of the electromagnet)
or a current flows through the electromagnet
or a (magnetic) field is produced

accept ‘electricity’ for ‘current’

accept the electromagnet is activated or magnetised or turned on

do not accept answer in terms of magnetic charge

1

the (iron) arm is attracted to the electromagnet

accept the arm pivots or moves towards the electromagnet

1

the contacts are pushed together

do not accept contacts attract

1

[4]

M10.          (i)      away from magnet

arrow should be perpendicular to field lines and current as judged by eye

1

(ii)      current in wire creates magnetic field around wire

1

two fields interact or combine giving a resultant force (on the wire)

1

[3]

M11.          (a)     (i)      one of the following:

•        increase number of turns on the secondary coil

•        decrease number of turns on the primary coil

1

(ii)     constructed in (thin) layers

1

(b)     (i)      transformers only work with a c

1

(ii)     used to increase or decrease or change voltage or current

reducing the energy or heat or power loss (along the cables)

1

or reduce to safe domestic level

must be consistent with first answer

1

(iii)     (several metres of) air gives good electrical 
insulation (between cables and earth) 
or reduce chance of earthing or sparks or arcing 
or to avoid people touching it

1

(c)     (i)

accept

or

1

(ii)     Np = 4000

for 1 mark

2

(d)     (i)      resistance of cable decreases

1

(ii)     convection (to the air)
or
conduction (to the air)

not radiation

1

[11]

M12.          (i)

accept input for primary

accept output for secondary

accept  or correct transposition

1

(ii)      60

allow 1 mark for correct transformation

2

[3]

M13.          (a)     plastic or rubber

accept any named plastic
do not accept wood

1

it is a (good) insulator or it is a poor conductor

ignore mention of heat if in conjunction with electricity

1

(b)     The answer to this question requires ideas in good English in a
sensible order with correct use of scientific terms. Quality of written
communication should be considered in crediting points in the mark scheme.

Maximum of 2 marks if ideas not well expressed.

pulls iron bolt down or attracts the iron bolt or moves bolt out of plunger

answers in terms of charges attracting
or repelling gain no credit

1

plunger pushed / moved to the right (by spring) or plunger released

1

push switch opens / goes to off / goes to right

accept circuit is broken

for maximum credit the points must follow a logical sequence

3 correct points but incorrect sequence scores 2 marks only

ignore reset action

1

[5]

M14.          (a)     10 500

allow 1 mark for 75 × 32 200 ÷ 230

2

(b)     any three from:

•        alternating current (a.c.) in the primary (coil)

•        produces a changing magnetic field / flux (in the core)

•        which is made of (laminated soft) iron

•        this induces

must be idea of inducing something in the secondary coil

•        an alternating potential difference across the secondary coil

accept voltage for potential difference

3

[5]

M15.          (a)     step-down (transformer)

1

(b)     alternating current

accept minor misspellings but
do not credit ‘alternative current’

1

(c)     (i)(ii)  magnet

attracts

upwards

correct order essential

accept ‘up’

3

[5]

M16.          (a)     (i)      step-down (transformer) because fewer turns on the output/secondary (coil)

no credit for just ‘step-down transformer’

accept ‘…less turns…’
do not credit ‘…fewer coils…’

or ‘the p.d. across the input / primary will be greater than the p.d. across the output / secondary’

1

(ii)     to prevent a short (circuit)(through the turns of wire or through the core

do not credit references to safety or heat (insulation)

1

(iii)     (easily) magnetised (and demagnetised)

accept ‘(it’s) magnetic’
do not accept ‘because it’s a conductor’

1

(b)     2250

correct substitution
eg  gains 1 mark

or appropriate transformation

eg (p.d. across secondary =)

× p.d. across primary gains 1 mark

2

(c)     any two from:

•        to reduce the voltage / p.d. (of the domestic supply)

or to reduce to 230 V
allow ‘to reduce to 240 V’
do not credit ‘reduce current to 230V’

•        higher voltage difficult to insulate

•        higher voltage (would) result in (fatal) electric shock

not just ‘less dangerous’

•        domestic appliances are not designed for (very) high
voltage (input) / (are designed) for 230V

do not credit ‘to increase efficiency’ / ‘to save energy’ do not credit just ‘it’s safer’

2

(d)     any two (1) each

•        if the (local) power station breaks down / fails / demand /
load exceeds supply

1

or words to that effect

•        electricity / power can be switched from elsewhere in the
system / from other power station(s)

or words to that effect

•        electricity can be generated in places remote from customers

or words to that effect

•        (in total) fewer power stations are needed

•        power available in rural / remote areas

•        National Grid allows for (better) control of supply and demand

do not credit just cheaper / more efficient / safer

1

[9]

M17.          (a)     increase the current (1)

credit increase the p.d./voltage
credit reduce the resistance
credit have thicker wiring
credit add extra / more cells

1

increase the magnetic field (strength) (1)

credit ‘have stronger magnet(s)
do not credit ‘bigger magnets’ either order

1

(b)     either reverse polarity

or connect the battery the other way round

1

either reverse direction of the magnetic field

or put the magnet the other way round / reverse the magnet

do not give any credit to a response in which both are done at the same time

either order

1

(c)     either

conductor parallel to the magnetic field

or lines of magnetic force and path of electricity do not cross

1

[5]

M18.          (a)     (i)      secondary(coil) / output (coil)

do not accept just coil

1

(ii)     core

do not accept for either mark it is made out of iron ore

1

(laminated soft) iron

allow 1 mark for ‘it is made out of iron core’

1

(iii)     magnetic field

accept magnetism / magnetic force

1

(which is) changing / alternating

direction (of field) changes / strength (of field) varies

scoring second mark is dependent on first mark

1

(b)     ...step-up .... step-down ...

both in the correct order

1

(c)     Do not build new houses ....

1

Build new power lines away ....

deduct 1 mark for any other(s) to a minimum total of (0)

1

[8]

M19.          (a)     (i)      (quickly) becomes magnetized

or (quickly) loses its magnetism

or ‘it’s (a) magnetic (material)’

any reference to conduction of electricity/heat nullifies the mark

1

(ii)     any four from:

•        insulation prevents electricity/current flowing through the iron/core

or ‘insulation so electricity/current only flows in the wires/turns/coils’

•        alternating current/a.c. in the primary (coil)

•        produces a changing magnetic field (in the iron/core)

•        (and hence magnetic) field in the secondary (coil)

•        induces/generates/produces an alternating potential difference/p.d./voltage across the secondary (coil)

•        (and hence) alternating current/a.c. in the secondary (coil)

4

(b)     80 (turns)

or credit (1) for any equation which if correctly evaluated would give 80 example

example

2

[7]

M20.          (a)     electric drill, electric fan, electric food mixer and electric screwdriver

all four ticked and no others (2)

either all four of these ticked and only one other (1)

or any three of these ticked and none/one/two of the others (1)

2

(b)     (i)      reverse (the direction of the) current (1)

or reverse the connections (to the battery)

reverse (the direction of the) magnetic field (1)

or reverse the (magnetic) poles /ends

do not credit ‘swap the magnets (around)’

2

(ii)     any two from:

•        increase the strength of the magnet(s)/(magnetic) field

do not credit ‘use a bigger magnet’

•        increase the current

allow ‘increase the voltage/p.d.’
allow add cells/batteries
allow increase the (electrical) energy
allow increase the power supply
allow ‘decrease the resistance’
allow ‘increase charge’
allow ‘ increase the electricity’

do not credit ‘use a bigger battery’

•        reduce the gap (between coil/armature
and poles/magnets)

allow increase the (number of) coils

•        increase the turns (on the coil/armature)

do not credit ‘use a bigger coil’

2

[6]

M21.          (a)     an alternating input / current to primary (coil)

1

which produces an alternating magnetic field

accept changing magnetic field for alternating magnetic field

if first mark point scores then ‘alternating’ not required here

1

in the (iron) core

this magnetic field links with the secondary coil

1

which induces an (alternating) voltage / p.d. across the
secondary (coil)

1

(b)     0.21

accept 0.2 or any answer that rounds to 0.21

allow 1 mark for correct equation
ie power input = power output

or

allow 1 mark for substitution into correct equation
ie 230 × Ip = 12 × 4

2

[7]

M22.          Marks awarded for this answer will be determined by the Quality of Written
Communication (QWC) as well as the standard of the scientific response.

No relevant content.

0 marks

There is a brief explanation of how a current is caused to flow in the 
starter motor circuit.

Level 1 (1–2 marks)

There is some explanation of how a current is caused to flow in the 
starter motor circuit.

Level 2 (3–4 marks)

There is a clear and detailed explanation of how a current is caused 
to flow in the starter motor circuit.

Level 3 (5–6 marks)

examples of the physics points made in the response

current flows through the coil / electromagnet

magnetic field produced

accept electromagnet switches on

(short side of) iron bar attracted to electromagnet

contacts pushed together (by iron bar)

starter motor circuit completed

current flows through starter motor

or

p.d. across starter motor

[6]

M23.          (a)     so the results can be compared fairly

fair test is insufficient

1

(b)     J L M

all 3 required and no other

1

(c)     (i)      for a given current the number of paper clips increases
by the same factor as the number of turns

1

plus a mathematical explanation using the data
eg a current of 1 A with 10 turns picks up 3 clips, a
current of 1 A with 20 turns picks up 6 clips

1

(ii)     30

allow 1 mark for showing correct use of figures eg
20 turns × 5 = 100 turns

2

(iii)     check the new data / repeat the experiment

1

to identify any anomalous results

1

then reconsider prediction / hypothesis in the
light of new evidence

1

[9]

M24.          (a)     (i)      must use an a.c.

1

(ii)     more than 30

1

(b)     iron

reason can only score if iron is chosen

1

because it can be magnetised (and demagnetised) easily

1

[4]