Q1.          The diagram shows two buses. Bus A is empty. Bus B contains bags of sand upstairs to represent passengers.

Each bus has been tilted as far as it can without falling over.

(a)     Each bus will topple over if it is tilted any further.

Explain, in as much detail as you can, why this will happen.

(You can draw on one of the diagrams as part of your answer if you want to.)

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(2)

(b)     What difference does it make to the stability of the bus when the upper deck is full of “passengers”? Explain your answer as fully as you can.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(3)

(c)     Why are the bags of sand in bus B only put upstairs?

....................................................................................................................................

....................................................................................................................................

(1)

(Total 6 marks)

Q2.          A spanner makes it a lot easier to loosen a bolt.

You cannot usually loosen                       It is easier
                       a bolt with your fingers.                     with a spanner.

Choose words from this list to complete the sentences below.

lever               piston               pivot               pulley               turning effect

The spanner is a simple ............................................................

You use it to produce a bigger ........................................................... on the bolt.

A longer spanner works better.

This is because there is a bigger distance between your force and the ...............................

(Total 3 marks)

Q3.          The diagram shows a simple machine for lifting water from a river.

(a)     Calculate the turning force (moment) of the bucket of water.

(Show your working.)

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

Answer .......................................................... Nm (newton metre)

(2)

(b)     What can you say about the size of downwards force the operator must use to balance the moment of the bucket of water?

(Explain your answer, using numbers if you can.)

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(4)

(Total 6 marks)

Q4.          A child stands a wooden brick on its end as shown in the diagram.

The child then pushes the brick to make it tilt.

How far must the brick be tilted to make it fall over?

Explain your answer.

(You may draw a labelled diagram if you wish.)

...............................................................................................................................................

...............................................................................................................................................

...............................................................................................................................................

(Total 2 marks)

Q5.          The diagram below shows the orbits for two types of satellite, a polar orbit and a geostationary orbit.

A satellite in stable Earth orbit moves at a constant speed in a circular orbit because there is a single force acting on it.

(i)      What is the direction of this force?

.....................................................................................................................................

(1)

(ii)      What is the cause of this force?

.....................................................................................................................................

(1)

(iii)     What is the effect of this force on the velocity of the satellite?

.....................................................................................................................................

(1)

(iv)     In which of the orbits shown above would this force be bigger?
Explain the reason for your answer.

.....................................................................................................................................

.....................................................................................................................................

(2)

(v)     Explain why the kinetic energy of the satellite remains constant.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 7 marks)

Q6.         The diagram below shows an outline of a balance. The balance is used to weigh lorries. A fraction of the weight of a lorry is used as the load on the right side of the pivot.

A standard weight W is moved along the arm until the weight of the load is balanced.

(a)     As the weight W is moved away from the pivot it can support a heavier load.
Why is this?

.....................................................................................................................................

.....................................................................................................................................

(2)

(b)     (i)      The weight W is 100 N. When it is 0.2 m from the pivot it balances the load.
Calculate the moment of the weight W about the pivot.

...........................................................................................................................

...........................................................................................................................

Answer ..................................... Nm

(2)

(ii)     The load is one hundredth of the weight of the lorry and is 0.02 m from the pivot.
Calculate the weight of the lorry.

...........................................................................................................................

...........................................................................................................................

Answer ..................................... N

(2)

(Total 6 marks)

Q7.          (a)     The diagram shows three similar toys. Each toy should be able to balance on a narrow rod. The arrows show the direction in which the weight of the toy acts.

Only one of the toys balances on the rod, the other two fall over. Which one of the toys is balanced? Explain the reason for your choice.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(b)     The diagram shows a simple toy. Different animal shapes can be positioned so that the 50 cm rod balances horizontally.

(i)      Use the following equation to calculate the moment exerted by the elephant shape of weight 2N about the pivot P. Show clearly how you work out your answer and give the unit.

moment = force × perpendicular distance from pivot

..........................................................................................................................

..........................................................................................................................

Moment = ...................................

(3)

(ii)     Use the following relationship to calculate the weight of the monkey shape.

total clockwise moment = total anticlockwise moment

..........................................................................................................................

..........................................................................................................................

Weight = ................................ N

(2)

(c)     The graph shows how the length of the spring changes as the total weight of the different animal shapes change.

Use the graph to find how much the spring extends when the elephant shape and the monkey shape are hung from the rod. Show how you get your answer.

.....................................................................................................................................

.....................................................................................................................................

Extension of spring = ................... cm

(2)

(Total 10 marks)

Q8.          For part of the ride the cyclist pushed on the pedals with a constant vertical force of 300 N. The simplified diagrams show the pedals in three different positions.

(i)      Which position, A, B, or C, gives the largest moment on the pedal?

.....................................................................................................................................

(1)

(ii)      Use the following equation to calculate, in Newton metres, the size of the largest moment on the pedal.

moment = force × perpendicular distance from pivot

.....................................................................................................................................

.....................................................................................................................................

Moment = ................................... Nm

(2)

(Total 3 marks)

Q9.          The diagram shows a spanner being used to undo a tight nut.

The nut was tightened using a moment of 120 newton metres.

Use the following equation to calculate the force needed to undo the nut. Show clearly how you work out your answer.

moment = force × perpendicular distance from pivot

...............................................................................................................................................

...............................................................................................................................................

Force = ............................................. N

(Total 2 marks)

Q10.          (a)     The diagrams show a windsurfer pulling up the sail of a sailboard. The mast pivots at point P.

In which position, A, B or C must the windsurfer pull with the largest force? Give a reason for your answer.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(b)     Once the mast is upright, the windsurfer and the sailboard are in equilibrium.

(i)      What does in equilibrium mean?

...........................................................................................................................

...........................................................................................................................

(1)

(ii)     The weight of the windsurfer is 700 newtons. Use the equation below to calculate the moment exerted by the windsurfer on the sailboard. Show clearly how you work out your answer.

moment = force × perpendicular distance from pivot

...........................................................................................................................

...........................................................................................................................

Moment = ......................................... Nm

(2)

(iii)     Use the relationship below to calculate the horizontal force of the wind on the sail. Show clearly how you work out your answer.

total clockwise moment = total anticlockwise moment

...........................................................................................................................

...........................................................................................................................

Force = ........................................ N

(2)

(c)     As the wind speed increases the windsurfer leans further out from the sailboard.

This position allows the windsurfer and sailboard to stay in equilibrium. Explain why.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(Total 10 marks)

Q11.          (a)     The diagram shows a lifebelt. It is hanging freely from hook Y.

(i)      On the diagram, mark with an X the point where you think the centre of mass of the lifebelt will be.

(1)

(ii)     Explain why you have chosen this point.

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

(2)

(b)     The drawing shows Susan on a diving board. She is 1.5 metres from point P and she weighs 500 N.

Calculate her moment (turning effect) about point P.
Show clearly how you work out your answer and give the unit.

.....................................................................................................................................

.....................................................................................................................................

Moment about P = ................................................

(3)

(c)     Susan has a case with wheels.

When she packs this case, she puts the heaviest items at the end where the wheels are.
This means that the heaviest items are less likely to crush the other contents and it helps her to find things when she opens the case.

Explain another advantage of packing her case in this way.

To gain full marks in this question you should write your ideas in good English. Put them into a sensible order and use the correct scientific words.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(4)

(Total 10 marks)

Q12.          (a)     A student has fastened a ball to a piece of string and is swinging it round in a horizontal circle.

(i)      The diagram below shows an overhead view of the movement of the ball.

Add an arrow, from the centre of the ball, to show the direction in which the ball would move if the string broke at this instant.

(1)

(ii)     Complete the table to show how force F changes if the student changes what he is doing. In each case, all the other factors stay the same.

| If the student | Force F needs to |
| --- | --- |
| uses a ball with a greater mass | ................................................. |
| swings the ball at a greater |  |
| speed | ................................................. |
| swings the ball with a shorter |  |
| piece of string | ................................................. |

(3)

(b)     The Moon orbits the Earth in a circular path. Use words from the box to complete the three spaces in the sentence.

direction resistance speed velocity

You may use each word once, more than once or not at all.

The Moon’s ................................. is constant but its .......................................... changes

because its .......................................... changes.

(2)

(c)     When any object moves in a circular, or nearly circular, path a force must act towards the centre of the circle.

(i)      What word is used to describe this force?

...........................................................................................................................

(1)

(ii)     The Moon orbits the Earth. What provides the force towards the Earth?

...........................................................................................................................

(1)

(iii)     In an atom, name the particles which are moving in circular paths around the nucleus.

...........................................................................................................................

(1)

(iv)    In the case of an atom, what word describes the forces which keep these particles moving in circular paths around the nucleus?

...........................................................................................................................

(1)

(Total 10 marks)

Q13.          Malik uses a camera to photograph the Moon.

(a)     Complete each sentence by choosing the correct words from the box.

You may use each word once, more than once or not at all.

| converging | diverging | image | longer |
| --- | --- | --- | --- |
| object | real | shorter | virtual |

In a camera a ........................................ lens is used to produce an ............................

of an ........................................ on a film. The ........................................ is smaller than

the ........................................ and it is a ........................................ distance from the lens.

(6)

(b)     The Moon moves in a nearly circular path around the Earth.

(i)      What is the name of the force which causes the Moon to move around the Earth?

...........................................................................................................................

(1)

(ii)     In which direction does this force act?

...........................................................................................................................

(1)

(c)     A force is needed to make a car change direction when it goes round a bend.

(i)      What is the name of this force and where does it act?

...........................................................................................................................

...........................................................................................................................

(2)

(ii)     Complete the two spaces in the sentence.

The force needed is greater if the ........................................ of the car is greater and

the ........................................ of the bend is smaller.

(2)

(d)     What word is used to describe any force which causes an object to move in a circular path?

....................................................................................................................................

(1)

(Total 13 marks)

Q14.          (a)     Every object has a centre of mass. What is meant by the centre of mass?

...................................................................................................................................

...................................................................................................................................

(1)

(b)     The drawing shows a thin sheet of plastic. The sheet is 250 mm wide. Two holes, each with a radius of 2 mm, have been drilled through the sheet.

Describe how you could use:

•        a clamp and stand

•        a steel rod 100 mm long and with a radius of I mm

•        a weight on a thin piece of string (= a plumb line)

•        a ruler

•        a pen which will write on the plastic sheet

to find the centre of mass of the plastic sheet.

To gain full marks in this question you should write your ideas in good English. Put them into a sensible order and use the correct scientific words.

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

...................................................................................................................................

(5)

(c)     There is a trapdoor in the ceiling of a house.
The trapdoor weighs 44 N.
The drawing shows a side view of the trapdoor.

(i)      Complete the three spaces to give the equation which is used to calculate the turning effect of a force.

......................... = ......................... × perpendicular between .........................
                                                 line of action and pivot

(1)

(ii)     Calculate the turning effect, about the hinge, due to the weight of the trapdoor.

Show clearly how you work out your final answer and give the unit.

.........................................................................................................................

.........................................................................................................................

Turning effect = ..............................................

(3)

(Total 10 marks)

Q15.          The London Eye is the largest observation wheel in the world.

The passengers ride in capsules. Each capsule moves in a circular path and accelerates.

(a)     Explain how the wheel can move at a steady speed and the capsules accelerate at the same time.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(2)

(b)     In which direction does each capsule accelerate?

....................................................................................................................................

(1)

(c)     What is the name of the resultant force that causes the capsules to accelerate?

....................................................................................................................................

(1)

(d)     The designers of the London Eye had to consider three factors which affect the resultant force described in part (c).

Two factors that increase the resultant force are

•        an increase in the speed of rotation

•        an increase in the total mass of the wheel, the capsules and the passengers.

Name the other factor that affects the resultant force and state what effect it has on the resultant force.

....................................................................................................................................

....................................................................................................................................

(1)

(Total 5 marks)

Q16.          The diagram shows a crane which is loading containers onto a ship.

(a)     Use the equation in the box to calculate the moment of the container which is being loaded.

| moment = force × | perpendicular distance from the line of action of the force to the axis of rotation |
| --- | --- |

Show clearly how you work out your answer and give the unit.

....................................................................................................................................

....................................................................................................................................

Moment of the container = .......................................................

(3)

(b)     Suggest and explain the purpose of the large concrete blocks.

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

....................................................................................................................................

(3)

(Total 6 marks)

Q17.          A girl and her father visit a children’s playground.

(a)     The diagram shows the girl holding on to a roundabout which is turning.

A centripetal force must act because the girl moves in a circular path.

(i)      In which direction, P, Q, R or S, does the centripetal force act?

Direction ..........

(1)

(ii)     What provides this centripetal force?

..........................................................................................................................

..........................................................................................................................

(1)

(iii)     Her father pushes the roundabout so that it turns faster. The girl continues to stand on the same part of the roundabout.

Complete the following sentence by drawing a ring around the correct line in the box.

| The centripetal force on the girl | decreases does not change increases |
| --- | --- |

(1)

(b)     The diagram shows the girl and her father on a see-saw.

(i)      Use the equation in the box to calculate the moment of the girl.

moment = force × perpendicular distance from the line of action of the force to the axis of rotation

..........................................................................................................................

..........................................................................................................................

Moment of the girl = ....................................... Nm

(2)

(ii)     What must her father do to increase his moment?

..........................................................................................................................

..........................................................................................................................

(1)

(c)     The diagram shows part of a level road that they take when they drive home. They drive at a steady speed.

(i)      At which point, A, B, C or D, will the centripetal force on the car be greatest?

Centripetal force is greatest at .................... .

(1)

(ii)     What provides the centripetal force when the car goes round a bend?

..........................................................................................................................

..........................................................................................................................

(1)

(Total 8 marks)

Q18.          (a)     The diagram shows a lampshade hanging from the ceiling. Draw an X on the diagram so that the centre of the X marks the centre of the mass of the lampshade.

(1)

­

(a)           Complete the sentence using the correct word or phrase from the box.

above below to the left of to the right of

A suspended object will come to rest with its centre of mass directly

................................................. the point of suspension.

(1)

(c)     The diagrams show equipment that a student uses to find the centre of mass of a thin sheet of card.

Arrange these sentences in the correct order to describe how the student can find the centre of mass of the card.

The sequence starts with sentence D and finishes with sentence E.

A       A line is drawn on the card marking the position of the string.

B       The pin is put through one of the holes in the card and held in the boss.

C       This is repeated using the other hole.

D       Two holes are made in the card with each hole near to the edge of the card.

E       The centre of mass is where the lines cross on the card.

F       The weight is tied to the string and then the string is hung from the pin.

| D |  |  |  |  | E |
| --- | --- | --- | --- | --- | --- |

(3)

(Total 5 marks)

Q19.          Tractors are often used on sloping fields, so stability is important in their design.

On the diagram, the centre of the X marks the centre of mass of the tractor.

(a)     Explain why the tractor has not toppled over. You may add to the diagram to help you to explain.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(b)     Give two features of the tractor which affect its stability and state how each feature could be changed to increase the tractor’s stability.

Feature 1 .....................................................................................................................

.....................................................................................................................................

Feature 2 .....................................................................................................................

.....................................................................................................................................

(2)

(Total 5 marks)

Q20.          A spanner gives a turning effect to undo a nut.

(a)     Complete the sentence.

The turning effect of a force is called the .................................................... of the force.

(1)

(b)     The diagram shows a spanner being used.

Use the equation in the box to calculate the spanner’s turning effect in newton metres.

turning effect = perpendicular distance from the line of action of the force to the axis of rotation

Show clearly how you work out your answer.

.....................................................................................................................................

.....................................................................................................................................

Turning effect = .............................. Nm

(2)

(c)     Give two ways in which you can increase the spanner’s turning effect.

1 ..................................................................................................................................

2 ..................................................................................................................................

(2)

(Total 5 marks)

Q21.          The diagram shows two children playing with a toy called a swing ball. The ball is joined to a pole by a strong string. The children hit the ball so that it goes round in a circular path.

(a)     Which force causes the ball to move in a circle?

Draw a ring around your answer.

air resistance                tension               weight

(1)

(b)     Complete the sentences by ticking () the correct ending.

(i)      The force needed to make the ball move in a circular path is larger if

the speed of the ball is increased.

the speed of the ball is decreased.

the string is made longer.

(1)

(ii)     The continuous acceleration of a ball moving in a circular path changes

the speed of the ball.

the direction of the ball.

the weight of the ball.

(1)

(c)     Which of the following words is used to describe any force that causes an object to move in a circular path?

Draw a ring around your answer.

centripetal                    frictional             gravitational                   universal

(1)

(Total 4 marks)

Q22.          (a)     The diagram shows a rectangle made out of a sheet of cardboard.

Draw an X on the diagram so that the centre of the X is at the centre of mass of the rectangle.

(1)

(b)     The drawing shows a car tyre.

(i)      Where is the centre of mass of the tyre?

...........................................................................................................................

(1)

(ii)     Explain your answer to (b)(i).

...........................................................................................................................

...........................................................................................................................

(1)

(Total 3 marks)

Q23.          (a)     The diagram shows a child’s mobile. The mobile hangs from point P on the ceiling of the child’s bedroom.

(i)      Mark the position of the centre of mass of the mobile by drawing a letter X on the diagram. Do this so that the centre of the X marks the centre of mass of the mobile.

(1)

(ii)     Explain why you have chosen this position for your letter X.

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

...........................................................................................................................

(2)

(b)     The diagram shows a device which helps to prevent a ladder from falling over.

Use the term centre of mass to explain why the ladder, in the situation shown, is unlikely to topple over.
You may add to the diagram to illustrate your explanation.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(3)

(Total 6 marks)

Q24.          The drawing shows a set of carriages on a roller coaster.
The carriages are moving upwards in a nearly circular path at a constant speed.

(a)     Complete the following sentences by drawing a ring around the correct line in each box.

| (i) The carriages will accelerate because of a change in their | direction mass speed | . |
| --- | --- | --- |

(1)

(ii)     The resultant force which causes the carriages to accelerate is the

| circular centripetal gravity | force. |
| --- | --- |

(1)

(b)     In which direction, A, B, C or D, does the resultant force act?

Write your answer in the box.

(1)

(c)     Complete the following sentence by drawing a ring around the correct line in the box.

| The resultant force will need to be greater if the | mass of the passengers is greater radius of the circle is greater speed of the carriages is less | . |
| --- | --- | --- |

(1)

(Total 4 marks)

Q25.          The drawing shows a sign which hangs outside a shop.

(a)     Draw an X on the sign so that the centre of your X is at the centre of mass of the sign.

(1)

(b)     Use a ruler to draw one axis of symmetry on the sign.

(1)

(c)     One force which acts on the sign is its weight.

Complete the following sentence by drawing a ring around the correct line in the box.

| The moment of the weight produces | an accelerating a balancing a turning | effect. |
| --- | --- | --- |

(1)

(Total 3 marks)

Q26.          This page is from a science magazine.

The Red Planet The two natural satellites, or moons, of Mars are Phobos (fear) and Deimos (terror). They are named after the horses which pulled the chariot of Mars, the god of war in the mythology of Ancient Greece. Phobos takes less than eight hours to orbit Mars and gets slightly closer every time it does so. Scientists predict that in about 100 million years time it will either be ripped apart by the gravitational force or will crash onto the surface of Mars.

(a)     Suggest how scientists have arrived at their prediction of about 100 million years.

.....................................................................................................................................

.....................................................................................................................................

(2)

(b)     The centripetal force on Phobos is gradually changing as it orbits Mars.

Is the force increasing or decreasing?

.....................................................................................................................................

Explain your answer.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(c)     Scientists expect that the mass of Mars and the mass of Phobos will not increase.

Explain what will happen to the gravitational force on Phobos as it orbits Mars.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 6 marks)

Q27.          The diagram shows a small mobile crane. It is used on a building site.

The distance, d, is measured to the front of the cab.

The table shows information from the crane driver’s handbook.

| Load in kilonewtons (kN) | Maximum safe distance, d, in metres (m) |
| --- | --- |
| 10 | 6.0 |
| 15 | 4.0 |
| 24 | 2.5 |
| 40 | 1.5 |
| 60 | 1.0 |

(a)     What is the relationship between the load and the maximum safe distance?

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(b)     The crane driver studies the handbook and comes to the conclusion that a load of 30 kN would be safe at a distance, d, of 2.0 metres.

Is the driver correct?

Explain your answer.

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(c)     What is the danger if the driver does not follow the safety instructions?

.....................................................................................................................................

.....................................................................................................................................

(1)

(d)     How should the data in the table have been obtained?

Put a tick () in the box next to your answer.

| average results from an opinion poll of mobile crane drivers |  |
| --- | --- |
| copied from a handbook for a similar crane |  |
| results of experiments on a model mobile crane |  |
| results of experiments on this mobile crane |  |

(1)

(Total 6 marks)

Q28.          (a)     Complete the following sentence by drawing a ring around the correct line in the box.

| A racing car can accelerate by changing | its direction only its speed only either its direction or its speed | . |
| --- | --- | --- |

(1)

(b)     A racing car moves round a circular part of a racetrack.

A force acts on the racing car. The force is towards the centre of the circular part of the racetrack.

Complete the following sentences by drawing a ring around the correct line in each of the boxes.

(i)

| The force is caused by | electrostatics friction gravity | . |
| --- | --- | --- |

(1)

(ii)

| The force is a | centripetal force circular force perpendicular force | . |
| --- | --- | --- |

(1)

(iii)     If another racing car has a greater mass and travels at the same speed

| around the same racetrack, then the force will need to | decrease stay the same increase | . |
| --- | --- | --- |

(1)

(iv)

| When the racing car goes faster, the force will need to | decrease stay the same increase | . |
| --- | --- | --- |

(1)

(c)     This is an item from a newspaper.

No to racetrack plan At last night’s meeting, one local resident said, “The racetrack will be noisy but motor racing leads to safety improvements in all our cars.’’ “We’ll need better brakes. Motor racing encourages speeding and leads to more accidents’’, said another. Most of the residents were against the plan to build a racetrack.

Do you agree with most of the residents?

Put a tick () in the box next to your answer and explain.

Yes                     No                  Not sure

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

.....................................................................................................................................

(2)

(Total 7 marks)

Q29.          A student wants to weigh himself but the only balance available is a newtonmeter that measures up to 200 newtons.
The diagram shows how the student solved the problem using moments.

(a)     Use the information in the diagram to calculate the weight of the student given by this method.

Write down the equation you use, and then show clearly how you work out your answer and give the unit.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

Weight = ....................................

(5)

(c)     Even though all the measurements are accurate the student’s weight obtained by this method is inaccurate.

Explain why.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

(2)

(Total 7 marks)

Q30.          A student wants to weigh himself but the only balance available is a newtonmeter that measures up to 200 newtons.
The diagram shows how the student solved the problem using moments.

(a)     Use the information in the diagram to calculate the weight of the student given by this method.

Write down the equation you use, and then show clearly how you work out your answer and give the unit.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

Weight = ....................................

(5)

(c)     Even though all the measurements are accurate the student’s weight obtained by this method is inaccurate.

Explain why.

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

........................................................................................................................

(2)

(Total 7 marks)

M1.          (a)     idea

•        line of action of weight/force/gravity
(if drawn: a vertical line through the centre of mass)

•        falls outside the (wheel) base (mark NOT from diagram)

for 1 mark each

2

(b)     ideas that

•        less stable/topples more easily

•        centre of mass at a higher level

•        so need small angle to make line of action of weight fall outside
(wheel) base

for 1 mark each

3

(c)     idea that

this is the most unstable condition (when bus used)
or
this makes c. of m. as high as it is likely to be

for 1 mark

1

[6]

M2.          lever

turning effect

pivot

for 1 mark each

[3]

M3.          (a)     evidence of moment = force × distance 
or 200 × 1.5

gains 1 mark

but 300

gains 2 marks

2

(b)     ideas that smaller than load

gains 1 mark

but 100 N or half the load

gains 2 marks

because applied further from pivot

gains 1 mark

but applied 2 × distance from pivot or evidence of balancing moments

gains 2 marks
(working for (b) shown in (a) gains credit – transfer mark)

4

[6]

M4.          any evidence of idea that weight acts through/near centre of mass/gravity/brick

gains 1 mark

but clear indication that brick topples if
vertical line through centre of mass is outside base line of brick
or line of action of weight is outside base line of brick

gains 2 marks

[2]

M5.          (i)      towards Earth

for 1 mark

1

(ii)      gravity

for 1 mark

1

(iii)     changes direction

for 1 mark

1

(iv)     polar orbit;
closer

for 1 mark each

2

(v)     speed constant (1)
mass constant (1)

for 1 mark each

2

[7]

M6.          (a)     moment/torque increases as moves away

gains 2 marks

leverage/force increases as moves away

gains 1 mark

2

(b)     (i)      20

gains 2 marks

else working

gains 1 mark

2

(ii)     100 000 ecf

gains 2 marks

else working

gains 1 mark

2

[6]

M7.          (a)     Z

1

weight or mass acts through pivot

accept rod or base for pivot

accept centre of gravity in line with pivot

1

no (resultant) (turning) moment

accept clockwise moment equals anticlockwise moment

do not accept same weight on each side of rod

1

(b)     (i)      30

allow 1 mark for 2  15

or 2  0.15

2

N cm

or

for full credit the unit must be consistent with the numerical answer

0.3

Nm

do not accept joules

1

(ii)     1.5 (N)

allow 1 mark for correct transformation

allow 2 marks ecf their part (b)(i)/20 (ecf only if correct physics)

2

(c)     5 (cm)

allow 1 mark for 6.0 (cm)

allow 1 mark for a subtraction of 1 from a value clearly obtained from the graph

allow 2 marks for correct ecf using an incorrect value for (b)(i)  0.2cm

allow 1 mark for clearly showing correct use of graph using an incorrect value for (b)(ii)

2

[10]

M8.          (i)      C

1

(ii)      48

an answer of 4 800 gains 1 mark

if answer (b)(i) is given as A then 42 scores 1 mark
4200 scores 0 marks substitution of correct figures = 1 mark

2

[3]

M9.          300

allow 1 mark for rearranging equation or correct substitution

[2]

M10.          (a)     A

must be correct for reason to score

moment (due to weight) of sail is the largest

1

or

(perpendicular) distance from pivot to rope the smallest

do not accept sail is low or sail is too heavy

1

(b)     (i)      no resultant turning moment or in a state of balance or balanced

allow clockwise moments = 
anticlockwise moments
allow no resultant force
allow (forces are) balanced
allow no acceleration
do not allow forces are equal

1

(ii)     moment = 420

allow 1 mark for moment = 700 × 0.6
or
700 × a distance from diagram (1.5, 2.1, 0.9)

2

(iii)     force = 280

420 = F × 1.5

or

F =  1 mark only

if (b)(ii) obtained by a correct method (1470, 630, 1050)

2

(c)     (as wind speed increases) the force on the sail increases

accept pressure

1

aniticlockwise moment increases or moment on sail increases

1

so clockwise moment (or opposite moment) needs to increase (by increasing
the distance from the pivot)

1

[10]

M11.          (a)     (i)      X at the centre of the lifebelt

measuring from the centre of X, allow 2 mm tolerance 
in any direction

1

(ii)     any two from:

if X is on vertical line below the hanger (but not at 
centre) can gain the first point only

below the point of suspension

accept ‘(vertically) below Y’

at the centre (of the lifebelt)

accept ‘in the middle’

(because) the lifebelt / it is symmetrical

or  (because) the mass / weight is evenly distributed

2

(b)     Nm or newton metre(s)

accept Newton metre(s)
do not accept any ambiguity in the symbol ie NM, nM or nm

1

750

(moment) = force  (perpendicular) distance (between line of action and pivot)
or  (moment) = 500  1.5 gains 1 mark

2

(c)     Quality of written communication:

for 2 of the underlined terms used in the correct context

1

any three connected points from:

low(er) centre of mass / gravity

or  centre of mass / gravity will be close(r) to the wheels 
/ axle / ground

(more) stable

or  less unstable

less likely to fall over

accept ‘less likely to overturn’
do not accept ‘will not fall over’

the turning effect / moment (of the weight of case) is less

or so less effort is needed to hold the case
ignore references to pulling the case

so the pull on her arm is less

3

[10]

M12.          (a)     (i)      arrow from centre of the ball and at right angles to the string
and in the correct direction

arrow should point to the student’s belt
accept free-hand ‘straight’ line 
do not accept curved line

1

(ii)     increase

accept ‘be stronger / bigger’

1

increase

accept ‘be stronger / bigger’

1

increase

accept ‘be stronger / bigger’

1

(b)     speed
velocity
direction

all three correct
any two correct for 1 mark
otherwise 0 marks

2

(c)     (i)      centripetal

accept ‘centripedal’ and other minor misspellings
do not accept anything which could be ‘centrifugal’

1

(ii)     gravity

accept ‘weight’
accept ‘force of attraction due to mass(es) (of the 
Moon and the Earth)’

1

(iii)     electron(s)

1

(iv)    electrostatic

accept ‘electrical’
do not accept just ‘centripetal’

1

[10]

M13.          (a)     converging

1

image

1

object

1

image

1

object

1

shorter

1

(b)     (i)      (Earth’s) gravity

accept centripetal 
accept minor misspellings, however, 
do not credit any response which could be ‘centrifugal’

1

(ii)     to(wards) (the centre of the) Earth

allow inwards do not accept downwards

1

(c)     (i)      either

friction (force) or  centripetal force

allow grip

1

between the tyres / wheels and (the surface of) the road

allow on the tyres / wheels 
or  towards the centre of the bend / arc / circle

1

(ii)     mass or speed or  momentum

allow weight allow velocity

1

radius / diameter

do not credit ‘curvature’ or ‘circumference’

1

(d)     centripetal

accept minor misspellings (see above)

1

[13]

M14.          (a)     point at which its mass (seems to) act or point at which gravity (seems to) act

accept ... its weight acts

accept correct statements if the intent is clear e.g.. .. if suspended, the centre of gravity will be directly under the point of suspension

e.g.... (if the object is symmetrical), the centre of gravity is on the or an axis (of symmetry)

do not credit just 'it is a point'

1

(b)     The answer to this question requires good English in a sensible order with correct use of scientific terms. Quality of written communication should be considered in crediting points in the mark scheme

maximum of 4 marks if ideas not well expressed

any five from:

clamp (steel) rod (horizontally)

no marks if method quite unworkable

hang plastic / sheet by rod through (one) hole

hang plumb line from rod

mark ends of plumb line on the sheet and
use the ruler to draw a straight line

repeat with other hole

centre of mass is where the lines cross

check by balancing at this point

maximum of 3 marks if no 'repeat with other hole'

5

(c)     (i)      (turning) effect or moment
force
distance

all three correct
accept weight
accept length

1

(ii)     17.6

allow 44 x 0.4 or 0.4 x 44 for 1 mark

2

Nm or newton metre(s)

do not accept N/m or N/cm

1760 Ncm gains all 3 marks

1

[10]

M15.          (a)     any two ideas:

•        (acceleration occurs when) the direction (of each capsule) changes

•        velocity has direction

•        acceleration is (rate of) change of velocity

2

(b)     to(wards) the centre (of the wheel)

1

(c)     centripetal

allow minor misspellings but do not credit a response which could be ‘centrifugal’

1

(d)     the greater the radius / diameter / circumference (of the wheel)
the smaller the (resultant) force (required)

accept ‘the size’

both parts required for the mark

accept converse

1

[5]

M16.          (a)     810 000

allow 45 000 × 18 for 1 mark

2

newton-metres / Nm

1

(b)     any three from:

ignore references to force throughout

•        their weight / mass can be altered / adjusted

•        so that the crane remains stable

allow does not topple

•        so that the (total) clockwise moment equals the (total)
anticlockwise moment

do not allow just ‘moments are equal’

•        because not all containers are the same weight / mass

do not allow ‘not all containers are the same size / volume’

•        because not all containers will be / need to move the same
distance (from the crane)

•        to keep the centre of mass (of the upper crane and container) in/
above the base of the tower

•        so that the crane remains in equilibrium/balanced

3

[6]

M17.          (a)     (i)      P

1

(ii)     the child’s grip / hold / pull (on the roundabout / bar / rail)

or ‘the tension in the child’s arms’

accept ‘the child’s muscles’

accept ‘friction between the child and the roundabout’

do not accept just ‘friction’

1

(iii)     increases

accept any unambiguous indication that this ending has been selected

1

(b)     (i)      360 (Nm)

credit either 240 × 1 ½

or 240 × 1.5 with 1 mark

2

(ii)     move to(wards) the left / to(wards) the / his end

or move away from the centre / pivot / axis (of rotation)

or move away from the girl / the child / his daughter

1

(c)     (i)      C

1

(ii)     friction / grip of the car / tyres / wheels (on the road)

do not accept just ‘friction / grip’

1

[8]

M18.          (a)     centre of X should appear to be on the continued line of the flex and in the
body of the lamp as judged by eye

example

1

(b)     below

1

(c)     (D)→B→F→A→C→(E)

all four correct for 3 marks

or any two correct for 2 marks

or just one correct for 1 mark

3

[5]

M19.          (a)     (line of action of) its weight

1

falls inside its wheel base

accept ‘falls between the wheels’

the first two points may be credited by adding a vertical line from the centre of the X on the diagram (1)
and labelling it weight / force / with a downwards arrow (1)
provided there is no contradiction between what is added to the diagram and anything which may be written

1

(so there is) no (resultant / clockwise) moment / turning effect

1

(b)     centre of mass should be lower

accept ‘… centre of gravity’
accept ‘weight / mass low down’
not just ‘lower the roof’

1

wheel base should be wider

accept ‘long axle(s)’ for ‘wide wheel base’
allow bigger / larger wheel base
do not credit ‘long wheel base’

responses in either order

1

[5]

M20.          (a)     moment

or torque do not credit ‘leverage’

1

(b)     4 (2)

either 0.20 × 20 (1) or allow ‘400’ (1)

2

(c)     use a longer spanner

or increases the perpendicular distance / length

or ‘fit a pipe over the (end of the) spanner (to lengthen it)’

note ‘lever’ refers to ‘spanner’
note change the . . . (0)
ignore references to wider / larger nut

1

use a greater force / pull

either order

1

[5]

M21.          (a)     tension

accept any unambiguous method of indication eg it’s underlined or ticked

1

(b)     (i)      speed of the ball is increased

1

(ii)     the direction of the ball

1

(c)     centripetal

accept any unambiguous method of indication
eg it’s underlined or ticked

1

[4]

M22.          (a)     centre of X at the point where the axes cross

to within 1 mm in any direction

1

(b)     (i)      (at / in the) centre (of the tyre)

or unambiguously shown on the diagram

1

(ii)     (this is) where axes of symmetry (of the tyre) cross / intersect / meet

or point at which the mass of the tyre seems to be (concentrated)

1

[3]

M23.          (a)     (i)      centre of X directly below P and between the model aeroplanes

as judged by eye but between centre of propeller of top aeroplane and canopy of bottom aeroplane

example

1

(ii)     the centre of mass is (vertically) below the point of suspension / P

1

the centre of mass is in the middle of the aeroplanes

accept the centre of mass is level with the aeroplanes

1

(b)     centre of mass of the worker and the ladder (and device)

1

line of action of the weight is inside the base

accept the centre of mass is above / within / inside the base (of the ladder and device)

1

so there will not be a (resultant) moment

accept so he / it / the ladder will not topple even if he leans over

or it will (only) topple over if the line of action of the weight / the
centre of mass is outside the base

accept each point, either on the diagram or in the written explanation, but do not accept the point if there is any contradiction between them

1

[6]

M24.          (a)     (i)      direction

accept any unambiguous indication

1

(ii)     centripetal

accept any unambiguous indication

1

(b)     A

accept any unambiguous indication

1

(c)     mass of the passengers is greater

accept any unambiguous indication

1

[4]

M25.          (a)     centre of X at the centre of the concentric circles

judge by eye that the intention is correct

1

(b)     drawn from any corner to the diagonally opposite corner

judge by eye that the intention is correct

or from the mid-point of any side to the mid-point of the opposite side

if more than one axis of symmetry has been drawn,
accept only if both / all are correct

1

(c)     a turning

accept any unambiguous indication

1

[3]

M26.          (a)     (from present/recent) data/evidence/observations of (the rate of change in)
Phobos’/the moon’s orbit (1)

or appropriate example of data (1)

and its correct use (1)

(and) continued/extended/extrapolated
(the pattern/trend for the next 100 million years) (1)

example (present) distance from Phobos to Mars (1) 
÷ (average) rate of approach (1)

2

(b)     (it is) increasing (1)

Phobos/the moon will be nearer (to Mars) (1)

or the radius/circumference/diameter of the orbit of Phobos/the moon will decrease/be less

only credit 2nd mark if the first mark is correct

2

(c)     it will increase/be more (1)

(because) Phobos/the moon will get/be closer to Mars/the planet (1)

only credit 2nd mark if the first mark is correct

note part(s) of this response may be included as the answer to part (b)

read both before marks are awarded

2

[6]

M27.          (a)     any two from:

•        inversely proportional

•        as the load gets biggerthe (maximum safe) distance gets less

allow ‘as the mass increases the distance decreases’
accept an unspecified response e.g. ‘big load at a short distance’ for (1)

•        load × distance = 60 (kNm)

2

(b)     yes, because 30 × 2 = 60 (2)

accept for (1) a correct but insufficiently explained response
e.g. ‘yes because it’s safe’

accept for (2) a correct response which is sufficiently explained

e.g. ‘yes, because 60 (kNm) at 1 metre is safe and 30 (kNm) is half the load at twice the distance

do not accept ‘no’ and do not accept just ‘yes’

do not accept ‘yes, because 30 is between 24 and 40 and 2 is between 2.5 and 1.5’

do not accept ‘the crane/ cable may break’ or other dangers

2

(c)     the crane may/will topple over/fall over/forward

1

(d)     results of experiments on this mobile crane

accept any unambiguous indication

1

[6]

M28.          (a)     either its direction or its speed

1

(b)     (i)      friction

1

(ii)     centripetal

1

(iii)     increase

1

(iv)    increase

1

(c)     examples

(yes) noisy (1)

disturbs people living nearby (1)

(yes) encourages people to drive fast (1) which makes (road) accidents more serious/likely (1)

(no) leads to improvements in safety features (1) such as better brakes (1)

(don’t know) noisy (1) but new tyres have a better grip (1)

whichever box has been ticked, the mark(s) is/are for an appropriate response

note, accept responses which assume that the public may use the racetrack

2

[7]

M29.          (a)     560

allow 1 mark for

clockwise (moments) = anticlockwise (moments)

allow 1 mark for correct substitution

ie 160 × 1.75 = W × 0.5

allow 1 mark for correct transformation

ie

4

newtons, N

1

(c)     the weight of plank which has been ignored

1

causes an anticlockwise moment which has not been
considered / included in the calculation

1

[7]

M30.          (a)     560

allow 1 mark for

clockwise (moments) = anticlockwise (moments)

allow 1 mark for correct substitution

ie 160 × 1.75 = W × 0.5

allow 1 mark for correct transformation

ie

4

newtons, N

1

(c)     the weight of plank which has been ignored

1

causes an anticlockwise moment which has not been
considered / included in the calculation

1

[7]